16 Tap FIR Filter
Omar F. Mousa/Chintan Daisa
Professor: Scott Wakefield

---
Design Objectives
Design Objectives
- To have a register based storage of 16 latest input values and the 16 impulse response coefficients on-chip.
- To utilize a clocked architecture to synchronize input and output values.
- Reduce the Number of Multiplier and Adder needed that is Optimize area and Power and cost.
- By Achieving the above the speed will not be compromised

---
Design Objectives
- Future scalability for input data as well as coefficient bits.
- Signed or unsigned input data as well as coefficients.
- Fast MAC operation on signed or unsigned data with future scalability.
- Synchronization of Input/Output data
- Configurable Output Precision

---
Design Objectives
- 16 taps of delay line.
- 8 bits of Input/Output bit resolution
- Burst mode of data transfer at Input supporting 32 elements of the desired resolution in one burst
Main Issue of concern when designing FIR Filter
Sharp Response
Number of Taps
Numerical Precision
Fully Parallel

---
Advantages and Disadvantages
Advantages:
Always stable (assume non-recursive implementation).
Quantization noise is not much of a problem.
Transients have a finite duration.
Disadvantages:
A high-order filter is generally needed to satisfy the stated specification – so more coefficients are needed with more storage and computation.

---
Review of discrete-time systems
Review of discrete-time systems
Linear time-invariant (LTI) systems
Causal systems:
for all input x[k]=0, k<0 -> output y[k]=0, k<0
Impulse response :
input 1,0,0,0,... -> output h[0],h[1],h[2],h[3],...
input x[0],x[1],x[2],x[3] -> output y[0],y[1],y[2],y[3],...
size 12{y \[ k \] = Sum cSub { size 8{i} } {u \[ i \] "." h \[ k - i \] } =u \[ k \] *h \[ k \] } {}
x[k]
y[k]

---
Overview
Overview
FIR filter equation
y[n] = x[n] * h [n]
where n is the number of “taps” or coefficients in the FIR filter.
For a 16-tap FIR filter
y[n] = a0x[n] + a1x[n-1] + a2x[n-2] + a3x[n-3]+…+ a15x[n-15]

---
Different Filter Representations
Different Filter Representations
Block Diagram Representation
- Difference equation
- Recursive computation needs y[-1] and y[-2]
  For the filter to be LTI, y[-1] = 0 and y[-2] = 0
Transfer function
  Assumes LTI system

x[k]
y[k]
Unit
Delay
Unit
Delay
1/2
1/8
y[k-1]
y[k-2]

---
Discrete-Time Systems
Discrete-Time Systems
Z-Transform:
size 12{H \( z \) = Sum cSub { size 8{i} } {h \[ i \] "." z rSup { size 8{ - i} } } } {}
size 12{U \( z \) = Sum cSub { size 8{i} } {u \[ i \] "." z rSup { size 8{ - i} } } } {}
size 12{Y \( z \) = Sum cSub { size 8{i} } {y \[ i \] "." z rSup { size 8{ - i} } } } {}
size 12{ { left [ matrix { 1 {} # z rSup { size 8{ - 1} } {} # z rSup { size 8{ - 2} } {} # "." "." "." {} # z rSup { size 8{ - 5} } {} } right ] "." left [ matrix { y \[ 0 \] {} ## y \[ 1 \] {} ## y \[ 2 \] {} ## y \[ 3 \] {} ## y \[ 4 \] {} ## y \[ 5 \] } right ]} underbrace { size 20{Y \( z \) }} = { left [ matrix { 1 {} # z rSup { size 8{ - 1} } {} # z rSup { size 8{ - 2} } {} # "." "." "." {} # z rSup { size 8{ - 5} } {} } right ] "." left [ matrix { h \[ 0 \] {} # 0 {} # 0 {} # 0 {} ## h \[ 1 \] {} # h \[ 0 \] {} # 0 {} # 0 {} ## h \[ 2 \] {} # h \[ 1 \] {} # h \[ 0 \] {} # 0 {} ## 0 {} # h \[ 2 \] {} # h \[ 1 \] {} # h \[ 0 \] {} ## 0 {} # 0 {} # h \[ 2 \] {} # h \[ 1 \] {} ## 0 {} # 0 {} # 0 {} # h \[ 2 \] {} } right ]} underbrace { size 8{ size 20{H \( z \) "." left [ matrix { size 20{1} {} # size 20{z rSup { size 6{ - 1} } } {} # size 8{z rSup { size 6{ - 2} } } {} # size 8{z rSup { size 6{ - 3} } } {} } right ]}} } "." left [ matrix { u \[ 0 \] {} ## u \[ 1 \] {} ## u \[ 2 \] {} ## u \[ 3 \] } right ]} {}
size 12{Y \( z \) =H \( z \) "." U \( z \) } {}

---
Discrete-Time Systems
`Popular’ frequency responses for filter design :
low-pass (LP) high-pass (HP) band-pass (BP)
band-stop multi-band …
size 12{π} {}
size 12{π} {}
size 12{π} {}
size 12{π} {}
size 12{π} {}
size 12{π} {}

---
Digital Filter Specifications
Digital Filter Specifications
For example the magnitude response of a digital lowpass filter may be given as indicated below
size 12{ lline G \( e rSup { size 8{jω} } \) rline } {}

---
Structured Streams
Structured Streams
Hierarchical Structures:
  - Pipeline
  - SplitJoin
  - Feedback Loop

---
Different Strategies
Different Strategies
- Map filter per tile and run
  forever
- Pros:
  - No filter swapping overhead
  - Reduced memory traffic
  - Localized communication
  - Tighter latencies
  - Smaller live data set
Cons:
  - Load balancing is critical
  - Not good for dynamic behavior
  - Requires # filters ≤ # processing elements

---
Discrete-Time Systems
`FIR filters’ (finite impulse response):
- Moving average filters (MA)
- N poles at the origin z=0 (hence guaranteed stability)
- N zeros (zeros of B(z)), `all zero’ filters
- corresponds to difference equation
- Impulse response
size 12{H \( z \) = { {B \( z \) } over {z rSup { size 8{N} } } } =b rSub { size 8{0} } +b rSub { size 8{1} } z rSup { size 8{ - 1} } + "." "." "." +b rSub { size 8{N} } z rSup { size 8{ - N} } } {}
size 12{y \[ k \] =b rSub { size 8{0} } "." u \[ k \] +b rSub { size 8{1} } "." u \[ k - 1 \] + "." "." "." +b rSub { size 8{N} } "." u \[ k - N \] } {}
size 12{h \[ 0 \] =b rSub { size 8{0} } ,h \[ 1 \] =b rSub { size 8{1} } , "." "." "." ,h \[ N \] =b rSub { size 8{N} } ,h \[ N+1 \] =0, "." "." "." } {}

---
Speeding Up FIR Filter
Speeding Up FIR Filter
- FIR speed-up
- y(0) = c(0)x(0) + c(1)x(-1) + c(2)x(-2) + . . . + c(N-1)x(1-N);
- y(1) = c(0)x(1) + c(1)x(0) + c(2)x(-1) + . . . + c(N-1)x(2-N);
- y(2) = c(0)x(2) + c(1)x(1) + c(2)x(0) + . . . + c(N-1)x(3-N);
- . . .
- y(n) = c(0)x(n) + c(1)x(n-1) + c(2)x(n-2)+ . . + c(N-1)x(n-(N-1));
- Run MAC at double frequency, read two 32-bit numbers
- FIR filtering: two outputs in parallel
- Two outputs = 4N reads, 2N MAC’s, 2 writes

---
Direct Form Realization
Direct Form Realization
size 12{Δ} {} size 12{Δ} {} size 12{Δ} {} size 12{Δ} {}
u[k]
u[k-4]
u[k-3]
u[k-2]
u[k-1]
x
bo
+
x
b4
x
b3
+
x
b2
+
x
b1
+
y[k]

---
Retiming FIR Filter Realizations
Retiming FIR Filter Realizations
Select subgraph (shaded)
  - Remove delay element on all inbound arrows
  - Add delay element on all outbound arrows
size 12{Δ} {} size 12{Δ} {} size 12{Δ} {} size 12{Δ} {}
u[k]
u[k-4]
u[k-3]
u[k-2]
u[k-1]
x
bo
+
x
b4
x
b3
+
x
b2
+
x
b1
+
y[k]

---
Retiming
Retiming
size 12{Δ} {} size 12{Δ} {} size 12{Δ} {} size 12{Δ} {}
u[k]
u[k-1]
x
bo
+
x
b1
+
y[k]
u[k-3]
u[k-2]
x
b4
x
b3
+
x
b2
+

---
Four Tap Direct Form Realization
size 12{Δ} {} size 12{Δ} {} size 12{Δ} {}
u[k]
u[k-3]
u[k-2]
u[k-1]
x
bo
+
x
b3
x
b2
+
x
b1
y[k]
+

---
Transposed Direct-Form Realization
Transposed Direct-Form Realization
size 12{Δ} {} size 12{Δ} {} size 12{Δ} {} size 12{Δ} {}
u[k]
x
bo
+
y[k]
x
b1
+
x
b2
+
x
b3
+
x
b4

---
Lattice Form Realizations
Lattice Form Realizations
size 12{Δ} {} size 12{Δ} {} size 12{Δ} {} size 12{Δ} {}
u[k]
u[k-1]
u[k-2]
x
b1
+
x
b2
+
x
+
x
+
b3
u[k-3]
x
b3
+
b2
x
+
x
bo
+
y[k]
b4
x
+
u[k-4]
x
b4
b1
x
bo
y[k]
~

---
FIR Filter Realizations
FIR Filter Realizations
Lattice Form
u[k]
size 12{y \[ k \] =b rSub { size 8{0} } "." u \[ k \] +b rSub { size 8{1} } "." u \[ k - 1 \] + "." "." "." +b rSub { size 8{N} } "." u \[ k - N \] } {}
bo
y[k]
ko
k1
k2
k3
i.e. different software/hardware, same i/o-behavior
size 12{Δ} {}
+
+
x
x
size 12{Δ} {}
+
+
x
x
size 12{Δ} {}
+
+
x
x
size 12{Δ} {}
+
+
x
x
x
y[k]
~

---
Efficient Direct Form Realization
Efficient Direct Form Realization
Efficient Direct-Form realization.
bo
b1
b2
b3
b4
x
x
x
x
x
y[k]
+
+
+
+
size 12{Δ} {} size 12{Δ} {} size 12{Δ} {} size 12{Δ} {}
u[k]
+
size 12{Δ} {}
size 12{Δ} {}
size 12{Δ} {}
size 12{Δ} {}
+
+
+
+

---
Pin Diagram
Pin Diagram
Synthesis using Synopsys Design Compiler
Initial Target Frequency: 100 MHz (typical)
Drive
y[0]
y[2]
y[3]
y[4]
y[5]
y[6]
….
y[31]
y[1]
x[0]
x[1]
…..
x[15]
Reset
Coeffin
Din
Clk
Vdd
Gnd
16-bit
16-tap
FIR
Filter
a[0]
a[1]
…..
a[15]

---
Specifications
Specifications
Input Specifications
- 16-bit unsigned integers for data inputs.
- 16-bit unsigned integers for coefficients.
Output Specifications
32-bit unsigned integer output.

---
System Components
System Components
- Memory - Input and Coefficient
- Control - Mod-4 and Mod-8 counters
- 3-8 Decoder
- Combinational logic
Multiplier	- Radius-8 Booth multiplier
- Multiplier register
Adder	- 9-bit Carry Save adder
- Adder register
Output Register

---
Specifications
Drive Signal(Output Signal)
- A new output is available.
- Inputs or coefficients to be applied only when Drive is asserted.
- Coefficients
- Any coefficient changed implies a new filter definition.
- Input Memory cleared – new data to be entered.

---
Specifications
System Clock
- One clock-cycle for the filter = 32 input clock pulses.
- One Tap-cycle = 8 input clock pulses described as 8 phases.
- 4 such Taps for each output.
System Reset
Active High

---
System Timing
System Timing
mod8 counter states

Input or Coefficient memory enable
Multiplier propagation delay
Multiplier propagation delay
Multiplier Register enable
Add Register Enable
Output Register Enable


---
System Timing Strategy
System Timing Strategy
- Two phase clocking
- Generation of internal lower frequency clocks using mod-4 and mod-8 counters
- Each state of mod-4 counter used for computation of one filter tap
- Output available at the end of one cycle of mod-4 counter

---
2-Parallel FIR Filtering Structure
2-Parallel FIR Filtering Structure
H0
H1
H0
H1
+
D
+
y(2k)
y(2k+1)
x(2k)
x(2k+1)
z-2

---
Hardware-Efficient 2-Parallel FIR Filter
Hardware-Efficient 2-Parallel FIR Filter
- Y0 = X0 H0 + z-2X1H1
- Y1 = X0 H1 + X1 H0
= (H0 + H1) (X0 + X1) – H0X0 – H1X1
z-2
H0
H0+H1
H1
+
D
+
y(2k)
y(2k+1)
x(2k)
x(2k+1)
+
+

---
Savings in the New Structure
Savings in the New Structure
Originally,
  - 2N multiplications + 2(N-1) additions for two inputs
In the new structure
  - 3*(N/2) = 1.5N multiplication
  - 3(N/2 –1) + 4 = 1.5N + 1 additions

---
Design Flow FIR 16 Tap Delay
VHDL
Deign Entry
Functional
Verification
Synthesis
EDIF
Timing
Verification
Floor planning
SDF
PDEF
Parasitic
PDEF
Physical
Verification
Place & Route

---
The FIR Filter
The FIR Filter
Implementation of 16 Tap FIR Filter, the coefficients are represented as fixed point 16-bits 2’s complement numbers. It is assumed that either or both of the coefficients and data are fractional numbers.

---
FIR Filter(Critical Path)
FIR Filter(Critical Path)
In order to save area and improve the critical path performance, we decided to add the 12-bit sum and carry results of the multiplier during the accumulation operation. Therefore, the adder has to add three 12-bit numbers. To do that, the first stage of the adder is a 3-to-2 combiner, which is just a CSA. The next stage is a CPA (Carry Propagate Adder) arranged in a static Manchester carry chain form. The chain is divided into four sections, each one has three carry stages. Buffers are used between sections to reduce the overall delay.

---
Survey of  Multiplier
Survey of Multiplier
Combinational Multiplier: uses n adders, eliminates registers:

---
Multiplier Design
44 multiplication
X3 X2 X1 X0 multiplicand
Y3 Y2 Y1 Y0 multiplier
X3Y0 X2Y0 X1Y0 X0Y0
X3Y1 X2Y1 X1Y1 X0Y1
X3Y2 X2Y2 X1Y2 X0Y2
X3Y3 X2Y3 X1Y3 X0Y3
Z7 Z6 Z5 Z4 Z3 Z2 Z1 Z0 Result
P.P.

---
Radix-2 Unsigned Multiplication
Radix-2 Unsigned Multiplication
Use a single n-bit adder, three registers (P, A, B), and a testing circuit for A0
Initialization: Place the unsigned numbers in registers A and B. Set P to zero.
1: If A0 is 1,
then register B, containing bn-1bn-2...b0 is added to P;
otherwise 00...00 (nothing) is added to P. The sum is placed back into P.
2. Shift register pair (P, A) one bit right.
The last bit of A is shifted out (not used).

---
Array Multiplier
Array Multiplier
- Array multiplier is an efficient layout of a combinational multiplier.
- Array multipliers may be pipelined to decrease clock period at the expense of latency.

---
Array Multiplier Organization
Array Multiplier Organization
0 1 1 0
x 1 0 0 1
0 1 1 0
+ 0 0 0 0
0 0 1 1 0
+ 0 0 0 0
0 0 0 1 1 0
+ 0 1 1 0
0 1 1 0 1 1 0
Multiplicand
Multiplier
skew array
for rectangular
layout
Product

---
Unsigned Array Multiplier
Unsigned Array Multiplier
+
x0y0
x1y0
x2y0
xny0
0
x0y1
+
x1y1
0
+
x0y2
+
x1y2
+
0
+
P(2n-1)
P(2n-2)
P0

---
Array Multiplier Organization
tmult(M-1) tcarry +(N-1) tsum + tand
For small tmult, tcarry
tsum
Beneficial to make tcarry = tsum
 Differential Logic (DCVS)
Array Multiplier cell

Xi
Yi
Pin
Cout
Pout
FA
Pout
Cout
Pin
Cin
Cin
Xi Yi
Critical Path
N-1 P.P
M-1

---
Architecture of Array Multiplier












HA
HA
×
×
×
×
HA
HA
X3 X2 X1 X0
Y0
Y1
Y2
Y3
Z7 Z6 Z5 Z4 Z3
Z0
Z1
Z2

---
Advantages of Array Multiplier
Array multipliers
  - Partial product generation and accumulation are merged
  - Identical cells
  - High-rate pipelining
a4x2
a3x3
a2x4
p6
a4x1
a3x2
a2x3
a1x4
p5
a4
x4
a4x0
a3x1
a2x2
a1x3
a0x4
p4
a3
x3
a3x0
a2x1
a1x2
a0x3
p3
a2
x2
a2x0
a1x1
a0x2
p2
a1
x1
a1x0
a0x1
p1
a0
x0
a0x0
p0
a4x3
a3x4
p7
a4x4
p8
p9

---
Array Multiplier
  - Array multiplier for Unsigned numbers
a4x0
a3x0
a2x0
a1x0
a0x0
0
0
0
0
a4x1
a3x1
a2x1
a1x1
a0x1
a4x2
a3x2
a2x2
a1x2
a0x2
a4x3
a3x3
a2x3
a1x3
a0x3
a4x4
a3x4
a2x4
a1x4
a0x4
0
p9 p8 p7 p6 p5 p4 p3 p2 p1 p0

---
Array Multiplier for Two’s Complement
    - type I cell
      - ordinary full adder
    - type II cell
      - x + y - z = 2c - s
      s = (x + y - z) mod 2
      c = [(x + y - z) + s] / 2
      - type I cell with
      inverted z and s
      z=1-z’, s=1-s’
weight = -1
z
II
x
y
c
s
x + y - z 2c - s
0 0 0 0 0
0 0 1 0 1
0 1 0 1 1
0 1 1 0 0
1 0 0 1 1
1 0 1 0 0
1 1 0 1 0
1 1 1 1 1

---
Array Multiplier for Two’s Complement
    - type II’ cell :
      - - x - y + z = - 2c + s
       x + y - z = 2c - s
       identical to the type II cell
z
y
II’
x
c
s
weight = -2
weight = -1

---
Architecture of Carry-Save Multiplier
Carry-Save Multiplier
carry propagation : diagonally downwards
instead of to left
 Requires additional adder (vector-merging adder)
 You can make this final adder very fast
using CLA or CSA scheme
44 multiplier












ripple-carry based multiplier

---
Architecture of Carry-Save Multiplier
Carry-Save Multiplier (44)
















Critical path
Vector-merging adder
carry-save multiplier
tmult=(N-1) tcarry + tand + tvma

---
Baugh-Wooley Multiplier
Baugh-Wooley Multiplier
- Algorithm for two’s-complement multiplication.
- Adjusts partial products to maximize regularity of multiplication array.
- Moves partial products with negative signs to the last steps; also adds negation of partial products rather than subtracts.

---
Serial-Parallel Multiplier
Serial-Parallel Multiplier
- Used in serial-arithmetic operations.
- Multiplicand can be held in place by register.
- Multiplier is shifted into array.

---
Serial-Parallel Multiplier
Serial Multiplier
M+N bits M*N cycles
size 12{ Sum {} } {}
reset
Serial to parallel
register
G1
G2
Full adder
Co
Ci
Delay element ; F/F
S
N-1 stages
X
Y

---
Serial-Parallel Multiplier
Y0
Y1
Y2
Yn-1
X
size 12{ Sum {} } {}
size 12{ Sum {} } {}
size 12{ Sum {} } {}

---
Serial-Parallel Multiplier
X3Y0
X2Y0
X1Y0
X0Y0
X0Y1
X1Y1
X2Y1
X3Y1
X0Y2
X1Y2
X2Y2
X3Y2
X0Y3
X1Y3
X2Y3
X3Y3
P7 P6 P5 P4 P3 P2 P1 P0
Y0
Y1
Y2
Y3
X3
X2
X1
X0

---
Serial-Parallel Multiplier
alignl { stack { size 12{X= Sum cSub { size 8{i=0} } cSup { size 8{m - 1} } {X rSub { size 8{i} } 2 rSup { size 8{i} } } } {} # Y= Sum cSub { size 8{j=0} } cSup { size 8{n - 1} } {Y rSub { size 8{j} } 2 rSup { size 8{j} } } {} } } {} alignl { stack { size 12{P rSub { size 8{r} } =X cdot Y= Sum cSub { size 8{i=0} } cSup { size 8{m - 1} } {X rSub { size 8{i} } 2 rSup { size 8{i} } Sum cSub { size 8{j=0} } cSup { size 8{n - 1} } {Y rSub { size 8{j} } 2 rSup { size 8{j} } } } } {} # matrix { matrix { {} # {} } {} # {} # = Sum cSub { size 8{i=0} } cSup { size 8{m - 1} } { Sum cSub { size 8{j=0} } cSup { size 8{n - 1} } { \( X rSub { size 8{i} } Y rSub { size 8{j} } \) 2 rSup { size 8{i+j} } } } {} } {} # matrix { matrix { {} # {} } {} # {} # = Sum cSub { size 8{k=0} } cSup { size 8{m+n - 1} } {P rSub { size 8{k} } 2 rSup { size 8{k} } } {} } {} } } {}
+
Pi+1
Yi
Xi
Ci
Ci+1

---
The Architecture of the Booth Algorithm
The Architecture of the Booth Algorithm
The Booth Multiplier
  - High performance, low power multiplier units are necessary in many situations, such as DSP systems.

---
Carry Save Addition
X7 X6 X5 X4 X3 X2 X1 X0
Y0
Y1
Y2
……..
……..
……..
FA
FA
FA
Y7
FA
FA
FA
CLA adder
. . . . . . . . .

---
Booth’s Algorithm
Booth’s Algorithm

---
Booth Algorithm
1st order(radix-2)
2nd order(radix-4)
3rd order(radix-8)
4th order(radix-16)

---
Booth Encoding
Booth Encoding
- Encode a number by taking groups of 3 bits
  where each 3-bit group overlaps by 1 bit
- Consider multiplier B with (n + 1) bit
  - Pad B with 0 to match the first term
  - if B has an odd number of bits,
    then extend the sign BnBnBn-1...B00
alignl { stack { size 12{E rSub { size 8{j} } = - 2 cdot B rSub { size 8{i} } +B rSub { size 8{i - 1} } +B rSub { size 8{i - 2} } } {} # E rSub { size 8{j+1} } = - 2 cdot B rSub { size 8{i+2} } +B rSub { size 8{i+1} } +B rSub { size 8{i} } {} } } {}

---
Booth Multiplier
Booth Multiplier
- Encoding scheme to reduce number of stages in multiplication.
- Performs two bits of multiplication at once—requires half the stages.
- Each stage is slightly more complex than simple multiplier, but adder/subtracter is almost as small/fast as adder.

---
Booth Encoding
Two’s-complement form of multiplier:
  - y = -2nyn + 2n-1yn-2 + 2n-2yn-2 + ...
Rewrite using 2a = 2a+1 - 2a:
  - y = -2n(yn-1-yn) + 2n-1(yn-2 -yn-1) + 2n-2(yn-3 -yn-2) + ...
Consider first two terms: by looking at three bits of y, we can determine whether to add x, 2x to partial product.

---
Booth Actions
Booth Actions
yi yi-1 yi-2	increment
0 0 0	0
0 0 1	x
0 1 0	x
0 1 1	2x
1 0 0	-2x
1 0 1	-x
1 1 0	-x
1 1 1	0

---
Booth Multiplier
x8
………….
Inverter/shift
Booth
decoder
Wallace Tree
CLA
CLA
CLA
x
2x
x
2x
selector
4
x0
y0
y1
y2
y3
y4
y5
y6
y7
y8

---
  Array Multiplier Cell for Booth’s Algorithm
0
(-2A)i
(2A)i
(A)i
(-A)i
MUX
Full Adder
cout
sout
select
cin
sin

---
Sign Extension Reduction
S0 S0 S0 S0 S0 S0 S0 S0 - - - - - - - -
S1 S1 S1 S1 S1 S1 - - - - - - - -
S2 S2 S2 S2 - - - - - - - -
S3 S3 - - - - - - - -
Sign
extension
1 S3 1 S2 1 S1 1 S0+1

---
Wallace Tree
Wallace Tree
- Reduces depth of adder chain.
- Built from carry-save adders:
  - three inputs a, b, c
  - produces two outputs y, z such that y + z = a + b + c
Carry-save equations:
  - yi = parity(ai,bi,ci)
  - zi = majority(ai,bi,ci)

---
Wallace Tree Structure
Wallace Tree Structure

---
7-bit Wallace Tree Addition
7-bit Wallace Tree Addition

---
Wallace Tree Operation
Wallace Tree Operation
- At each stage, i numbers are combined to form ceil(2i/3) sums.
- Final adder completes the summation.
- Wiring is more complex.
- Can build a Booth-encoded Wallace tree multiplier.

---
CSA vs. Wallace Tree
C S
FA
FA
FA
FA
1
2
3
4
5
6
FA
FA
FA
FA
C S

---
Radix-4 Modified Booth’s Algorithm
    A 0 1 0 1 1 0 22
    X X 0 0 1 0 1 1 11
    Y(recoded multiplier) 0 1 0 1 0 1
1
1 0 0 1 0 1 0
1 0 0 1 0 1 0
1 1 1 0 1 1 0
1 0 0 0 1 1 1 1 0 0 1 0

---
Wallace-Tree
Wallace-Tree
Collapse the chain of FAs y0-y5 (5 adders delays) to the Wallace tree consisting of (4 adders delays)

---
Floor Plan of Multiplier
1) Square Floor Plan
X3 X2 X1 X0
X
Y0
Y1
Y2
Y3
Y
Z0
|
Z3
Z7 — Z4
Z7 Z6 Z5 Z4 Z3 Z2 Z1 Z0

---
Floor Plan of Multiplier
In The Actual Datapath
x
Y
LSB
L
S
B
MSB
M1
M2
or
M3

---
Floor Plan
Floor Plan
Adder
Add Reg
Out Reg
Multiplier
Multiplier Reg
Control Block
Coefficient Memory
Input
Memory
Routing

---
Floor Planning
Floor Planning

---
Results
Results
Cell	Number of Ports
Number of Ports	34
Number of Nets	157
Number of Cells	32
Combinational Area	24286.050781
Non-Combinational Area	14935.535156
Total Area	39221.585938

---
Power Consumption & Area
Power Consumption & Area
Cell Internal Power = 419.5078 uW (57%)
Net Switching Power = 315.0848 uW (43%)
Total Dynamic Power = 734.5925 uW (100%)
Cell Leakage Power = 248.1773 nW

---
Main Module
Main Module

---
Booth Multiplier

---
Core Module
Core Module

---
Controller Module
Controller Module

---
Conclusion
Conclusion
- Good Design Experience.
- Using Parallel FIR Filter Realization Reduced the number of Multiplier and Adder needed therefore Area was shrunk and power consumption was lowered
- Timing Strategies Using non-blocking in Verilog reduced number of states needed for implementation.
- Partitioning the design into submodules made design more manageable and optimized.
- Performance Optimization was reached with slack time equal to +9.54.